## Slide 1: network

## Slide 2: intro

## Slide 3: networking

## Slide 4: networking: enable machine-to-machine communication
goal: enable applications that span multiple computers
  websites
  streaming video
  email
  chat
  …
challenge: realities of the real-world
  massive scale
  consequences of success
  security
  geopolitical and economic concerns

## Slide 5: sockets

## Slide 6: sockets is the de-facto API for networking
open connection then …
  read+write just like a terminal file
doesn’t look like individual messages
‘‘connection abstraction’’

## Slide 7: mailbox model

## Slide 8: mailbox model
mailbox abstraction: send/receive messages

## Slide 9: connections over mailboxes
real Internet: mailbox-style communication
  send ‘‘letters’’ (packets) to particular mailboxes
  have ‘‘envelope’’ (header) saying where they go
‘‘best-effort’’
  no guarantee on order, when received
  no guarantee on if received
sockets implemented on top of this

## Slide 10: review: connection abstraction

## Slide 11: connections

## Slide 12: layers preview

## Slide 13: networking layers
application
HTTP, SSH, SMTP, …
application-defined meanings
transport
TCP, UDP, …
reach correct program reliability/streams
network
IPv4, IPv6
reach correct machine (across networks)
link
Ethernet, Wi-Fi, …
coordinate shared wire/radio
physical
Ethernet, Wi-Fi, …
encode bits for wire/radio

## Slide 14: layers terminology
application
application-defined meanings
transport
reach correct program, reliablity/streams
segments/datagrams
network
reach correct machine (across networks)
packets
link
coordinate shared wire/radio
frames
physical
encode bits for wire/radio

## Slide 15: layer wrapping

## Slide 16: layer encapsulation
upper layers implemented using lower layers
example: implement reliable + large messages (transport layer) by sending multiple unreliable messages across networks (network layer)
example: implement reaching machine across networks (network layer) by sending multiple messages on local networks (link layer)

## Slide 17: handling network failures

## Slide 18: reality: you don’t own the network!
the internet is a series of connected networks
packets traverse routers within and between networks
those networks provide ‘‘best-effort’’ service

## Slide 19: network limitations/failures
messages lost
messages delayed/reordered
messages limited in size
messages corrupted

## Slide 20: acknowledgments

## Slide 21: dealing with network message lost

## Slide 22: handling lost message: acknowledgements

## Slide 23: handling lost message

## Slide 24: exercise: lost acks

## Slide 25: exercise: lost acknowledgement

## Slide 26
exercise: how to fix this?
A.
machine A needs to send ‘‘Got ‘got it!’ ’’
B.
machine B should resend ‘‘Got it!’’ on its own
C.
machine A should resend the original message on its own
D.
none of these

## Slide 27: answers
send ‘‘Got ‘got it!’ ’’?
  same problem: Now send ‘Got Got Got it’?
resend ‘‘Got it!’’ own its own?
  how many times? — B doesn’t have that info
resend original message?
  yes!
  as far as machine A can see, exact same situation as losing original message

## Slide 28: solution: lost acks

## Slide 29: lost acknowledgements

## Slide 30: delayed acks

## Slide 31: delayed message

## Slide 32: delayed acknowledgements

## Slide 33: splitting into multiple

## Slide 34: splitting messages: try 1

## Slide 35
reconstructed message: The meeting is at 12pm.

## Slide 36: splitting messages: try 1 — problem 1

## Slide 37
reconstructed message: The meetingThe meeting is at 12pm.

## Slide 38: exercise: other problems?
other scenarios where we’d also have problems?
  1.
  message (instead of acknowledgment) is lost
  2.
  first message from machine A is delayed a long time by network
  3.
  acknowledgment of second message lost instead of first

## Slide 39: splitting messages: try 2

## Slide 40
reconstructed message: The meeting is at 12pm.

## Slide 41: splitting messages: try 2 — missed ack

## Slide 42
reconstructed message: The meeting is at 12pm.

## Slide 43: splitting messages: try 2 — problem

## Slide 44
A thinks: part 1 + part 2 acknowleged!

## Slide 45: splitting messages: version 3

## Slide 46: checksums

## Slide 47: message corrupted
corruption: e.g., a bit flip
  sent: I LIKE CATS (49204C494B452043415453)
  recv: I LIKE BATS (49204C494B452042415453)
instead of sending ‘‘message’’, send ‘‘message’’ + checksum
  checksum is some calculation using the original message
  ex: checksum(I LIKE CATS) = 0xD9
  send 49204C494B452043415453D9
receiver then also computes the checksum with the same data
  if matches: keep the message
  if does not match: pretend like the message was lost (i.e., drop the message)

## Slide 48: aside: going faster

## Slide 49: going faster
so far: send one message, wait for acknowledgment
very slow!
instead, can send a bunch of parts and get them acknowledged together

## Slide 50: transmission window (ex: size 4)

## Slide 51
Send a window of parts speculatively, then wait for ACKs.

## Slide 52: UDP v TCP

## Slide 53: transport layer protocols: UDP vs. TCP
TCP: stream to other program
  reliable transmission of as much data as you want
  ‘‘connecting’’ fails if server not responding
  write(fd, “a”, 1); write(fd, “b”, 1) = write(fd, “ab”, 2)
  (at least) one socket per remote program being talked to
UDP: messages sent to program, but no reliablity/streams
  unreliable transmission of short messages
  write(fd, “a”, 1); write(fd, “b”, 1) write(fd, “ab”, 2)
  ‘‘connecting’’ just sets default destination
  can sendto()/recvfrom() multiple other programs with one socket
    (but don’t have to)

## Slide 54: addresses versus names

## Slide 55: mailbox model: importance of naming
mailbox abstraction: send/receive messages

## Slide 56: names and addresses
name
address
logical identifier
location/how to locate
variable counter
memory address 0x7FFF9430
DNS name www.virginia.edu
IPv4 address 128.143.22.36
DNS name mail.google.com
IPv4 address 216.58.217.69
DNS name mail.google.com
IPv6 address 2607:f8b0:4004:80b::2005
DNS name cso2.cs.virginia.edu
IPv4 address 128.143.67.91
DNS name cso2.cs.virginia.edu
MAC address 18:66:da:2e:7f:da
service name https
port number 443
service name ssh
port number 22

## Slide 57: IP

## Slide 58: the network layer
the Internet Protocol (IP) version 4 or version 6
  there are also others, but quite uncommon today
allows send messages to/recv messages from other networks
  ‘‘internetwork’’
messages called ‘‘packets’’

## Slide 59: IPv4 addresses

## Slide 60: IPv4 addresses
32-bit numbers
typically written like 128.143.67.11
  four 8-bit decimal values separated by dots
  first part is most significant
  same as
organizations get blocks of IPs
  e.g. UVa has 128.143.0.0–128.143.255.255
  e.g. Google has 216.58.192.0–216.58.223.255 and 74.125.0.0–74.125.255.255 and 35.192.0.0–35.207.255.255
some IPs reserved for non-Internet use (127.10.x.x, 192.168.x.x)

## Slide 61: IPv6 addresses

## Slide 62: IPv6 addresses
IPv6 like IPv4, but with 128-bit numbers
written in hex, 16-bit parts, seperated by colons (:)
strings of 0s represented by double-colons (::)
typically given to users in blocks of or addresses
  no need for address translation?
2607:f8b0:400d:c00::6a = 2607:f8b0:400d:0c00:0000:0000:0000:006a
  2607f8b0400d0c0000000000000006a

## Slide 63: routing idea

## Slide 64: IPv4 addresses and routing tables

## Slide 65: lab API

## Slide 66: upcoming lab
request + receive message split into pieces
you are responsible for:
  requesting parts in order
  resending requests if messages lost/corrupted
‘‘acknowledge’’ receiving part X to request part X+1

## Slide 67: protocol
GET(x) — retrieve message (x = 0, 1, 2, or 3)
  other end acknowledges by giving data
  if they don’t reply, you need to send again
  higher numbered messages have errors/etc. that are harder to handle
ACK(n)
  request message part by acknowledging message part
  not quite same purpose as acknowledgments in prior examples
  (in lab, the response is your ‘acknowledgment’ of your request; you retry if you don’t get it)

## Slide 68: callback-based programming (1)
/* library code you don't write */ /* lab: part of waitForAllTimeoutsAndMessagesThenExit() */ void mainLoop() { while (notExiting) { Event event = waitForAndGetNextEvent(); if (event.type == RECIEVED) { recvd(...); } else if (event.type == TIMEOUT) { (event.timeout_function)(...); } ... } }

## Slide 69: callback-based programming (2)
/* your code, called by library */ void recvd(...) { ... setTimeout(..., timerCallback, ...); } void timerCallback(...) { ... } int main() { send(.../* first message */); ... /* other initial setup */ waitForAllTimeoutsAndMessagesThenExit(); // runs mainLoop() }

## Slide 70: callback-based programing (3)
packet = getNextPacket() doSomething(packet); sleep(10); doAnotherThing(); packet = getNextPacket(); doYetAnotherThing(packet);
turns into code like:
afterTimeout() { doAnotherThing(); mode = 2; } recvdPacket(packet) { if (mode == 1) { doSomething(packet); setTimeout(10, afterTimeout); } else if (mode == 2) doYetAnotherThing(packet); } else ... }

## Slide 71: callback-based programming uses
writing scripts in a webpage
many graphical user interface libraries
sometimes servers that handle lots of connections

## Slide 72: layers, revisited

## Slide 73: port numbers

## Slide 74: port numbers
we run multiple programs on a machine
  IP addresses identifying machine — not enough
so, add 16-bit port numbers
  think: multiple PO boxes at address
0–49151: typically assigned for particular services
  80 = http, 443 = https, 22 = ssh, …
49152–65535: allocated on demand
  default ‘‘return address’’ for client connecting to server

## Slide 75: OS tracking connections

## Slide 76: connections in TCP/IP
connection identified by 4-tuple
  used by OS to lookup ‘‘where is the socket?’’
(local IP address, local port, remote IP address, remote port)
local IP address, port number can be set with bind() function
  typically always done for servers, not done for clients
  system will choose default if you don’t

## Slide 77: DNS

## Slide 78: DNS: Domain Name System

## Slide 79: URLs and URIs

## Slide 80: URL / URIs
Uniform Resource Locators (URL)
  tells how to find ‘‘resource’’ on network
  uniform — one syntax for multiple protocols (types of servers, etc.)
Unifrom Resources Identifiers
  superset of URLs

## Slide 81: URI examples

## Slide 82: URI generally
scheme://authority/path?query#fragment
scheme: — what protocol
//authority/
  authoirty = user@host:port OR host:port OR user@host OR host
path
  which resource
?query — usually key/value pairs
#fragment — place in resource
most components (sometimes) optional

## Slide 83: HTTP

## Slide 84: HTTP: HyperText Transfer Protocol
primary application-layer protocol for the Web
standard port: 80 (non-encrypted), 443 (encrypted)
uses TCP (or TCP + TLS for encrypted version)
client-server protocol
  server = always on machine, never initiaites contact
  client = sometimes on machine, initiates contact
ex. URL: http://www.foo.com/bar

## Slide 85: HTTP: HyperText Transfer Protocol
http://www.foo.com/bar
HTTP client (example: web browser) connects via TCP to www.foo.com
sends something like
GET /bar HTTP/1.1 Host: www.foo.com ...
server replies with status code + (usually) some data
  200 OK, 403 Unauthorized 404 Not Found, 500 Internal Server Error, …

## Slide 86: HTTP miscellany
other HTTP commands besides GET
POST — sending forms
HEAD — get metadata about file (without getting its data)
PUT, DELETE, …
all requests/replies have many possible headers
  filetype inforation
  login-related information (usually)
  metadata used for caching webpages
  …

## Slide 87: NAT

## Slide 88: why IPv4 and IPv6?
ran out of IPv4 addresses
  seemed like a lot of addresses
  now there are more internet users than addresses
possible solutions:
\begin{enumerate} \item{} IPv6: use more bits for addresses, enough to never run out \item{} NAT: user one IPv4 address for an entire network of devices \end{enumerate}

## Slide 89: NAT: network address translation
convert many private addrs. to one public addr.
locally: use private IP addresses for local addresses
outside: private IP addresses become a single public one
commonly how home networks work (and some ISPs)
certain IPv4 address blocks reserved for private/internal use
  192.168.X.X
  172.16.X.X–172.31.X.X
  10.X.X.X
  …

## Slide 90: NAT idea

## Slide 91: NAT illusion
NAT illusion:
private IP address communicating directly with public IP
inside network, talking to outside:
  use private local address
  use public remote address
  never see router’s address
outside network, talking to inside
  use public local address
  use router’s public address

## Slide 92: implementing NAT
remote host + port
outside local port number
inside IP
inside port number
128.148.17.3:443
54033
192.168.1.5
43222
11.7.17.3:443
53037
192.168.1.5
33212
128.148.31.2:22
54032
192.168.1.37
43010
128.148.17.3:443
63039
192.168.1.37
32132
table of the translations
need to update as new connections made

## Slide 93: Backup slides

## Slide 94: The Internet
Perhaps the most successful computer application ever
Can you name a computer program that doesn’t use the internet?

## Slide 95
\begin{center} ![](/network/internet_users.png){} \end{center}

## Slide 96
\begin{center} ![](/network/internet_reasons.png){} \end{center}

## Slide 97
\begin{center} ![](/network/internet_data.png){} \end{center}

## Slide 98: ethernet / 802.11 /

## Slide 99: the link layer
Ethernet, Wi-Fi, Bluetooth, DOCSIS (cable modems), …
allows send/recv messages to machines on ‘‘same’’ network segment
  typically: wireless range+channel or connected to a single switch/router
  could be larger (if bridging multiple network segments)
  could be smaller (switch/router uses ‘‘virtual LANs’’)
typically: source+destination specified with MAC addresses
  MAC = media access control
  usually manufacturer assigned / hard-coded into device
  unique address per port/wifi transmitter/etc.
can specify destination of ‘‘anyone’’ (called broadcast)
messages usually called ‘‘frames’’

## Slide 100: link layer jobs
divide raw bits into messages
identify who message is for on shared radio/wire
handle if two+ machines use radio/wire at same time
drop/resend messages if corruption detected
  resending more common in radio schemes (wifi, etc.)

## Slide 101: exercise: why resend?

## Slide 102: link layer reliablity?
Ethernet + Wifi have checksums
Q1: Why doesn’t this give us uncorrupted messages?
  Why do we still have checksums at the higher layers?
Q2: What’s a benefit of doing this if we’re also doing it in the higher layer?

## Slide 103: link layer quality-of-service

## Slide 104: link layer quality of service
if frame gets…
event
on Ethernet
on WiFi
collides with another
detected + may resend
resend
not received
lose silently
resent
header corrupted
usually discard silently
usually resend
data corrupted
usually discard silently
usually resend
too long
not allowed to send
not allowed to send
reordered (v. other messages)
received out of order
received out of order
destination unknown
lose silently
usually resend??
too much being sent
discard excess?
discard excess?

## Slide 105: network layer quality-of-service

## Slide 106: network layer quality of service
if packet …
event
on IPv4/v6
collides with another
out of scope — handled by link layer
not received\tikzmark{not recv}
lost silently
header corrupted
usually discarded silently
data corrupted
received corrupted
too long
dropped with notice or ‘‘fragmented’’ + recombined
reordered (v. other messages)
received out of order
destination unknown
usually dropped with notice
too much being sent
discard excess

## Slide 107: firewalls

## Slide 108: firewalls
don’t want to expose network service to everyone?
solutions:
  service picky about who it accepts connections from
  filters in OS on machine with services
  filters on router
later two called ‘‘firewalls’’

## Slide 109: firewall rules examples?
ALLOW tcp port 443 (https) FROM everyone
ALLOW tcp port 22 (ssh) FROM my desktop’s IP address
BLOCK tcp port 22 (ssh) FROM everyone else
ALLOW from address X to address Y
…

## Slide 110: aside: TCP state machine

## Slide 111: TCP state machine
TIME_WAIT, ESTABLISHED, …?
OS tracks ‘‘state’’ of TCP connection
  am I just starting the connection?
  is other end ready to get data?
  am I trying to close the connection?
  do I need to resend something?
standardized set of state names

## Slide 112: TIME_WAIT
remember delayed messages?
problem for TCP ports
if I reuse port number, I can get message from old connection
solution: TIME_WAIT to make sure connection really done
  done after sending last message in connection

## Slide 113: TCP state machine picture

## Slide 114: DNS: DIG trace

## Slide 115: querying the root
$ dig +trace +all www.cs.virginia.edu ... edu. 172800 IN NS b.edu-servers.net. edu. 172800 IN NS f.edu-servers.net. edu. 172800 IN NS i.edu-servers.net. edu. 172800 IN NS a.edu-servers.net. ... b.edu-servers.net. 172800 IN A 191.33.14.30 b.edu-servers.net. 172800 IN AAAA 2001:503:231d::2:30 f.edu-servers.net. 172800 IN A 192.35.51.30 f.edu-servers.net. 172800 IN AAAA 2001:503:d414::30 ... ;; Received 843 bytes from 198.97.190.53#53(h.root-servers.net) in 8 ms ...

## Slide 116: querying the edu
$ dig +trace +all www.cs.virginia.edu ... virginia.edu. 172800 IN NS nom.virginia.edu. virginia.edu. 172800 IN NS uvaarpa.virginia.edu. virginia.edu. 172800 IN NS eip-01-aws.net.virginia.edu. nom.virginia.edu. 172800 IN A 128.143.107.101 uvaarpa.virginia.edu. 172800 IN A 128.143.107.117 eip-01-aws.net.virginia.edu. 172800 IN A 44.234.207.10 ;; Received 165 bytes from 192.26.92.30#53(c.edu-servers.net) in 40 ms ...

## Slide 117: querying virginia.edu+cs.virginia.edu
$ dig +trace +all www.cs.virginia.edu ... cs.virginia.edu. 3600 IN NS coresrv01.cs.virginia.edu. coresrv01.cs.virginia.edu. 3600 IN A 128.143.67.11 ;; Received 116 bytes from 44.234.207.10#53(eip-01-aws.net.virginia.edu) in 72 ms www.cs.Virginia.EDU. 172800 IN A 128.143.67.11 cs.Virginia.EDU. 172800 IN NS coresrv01.cs.Virginia.EDU. coresrv01.cs.Virginia.EDU. 172800 IN A 128.143.67.11 ;; Received 151 bytes from 128.143.67.11#53(coresrv01.cs.virginia.edu) in 4 ms

## Slide 118: querying typical ISP’s resolver
$ dig www.cs.virginia.edu ... ;; ANSWER SECTION: www.cs.Virginia.EDU. 7183 IN A 128.143.67.11 ..
cached response
valid for 7183 more seconds
after that everyone needs to check again

## Slide 119: UDP sockets

## Slide 120: ‘connected’ UDP sockets
int fd = socket(AF_INET, SOCK_DGRAM, 0); struct sockaddr_in my_addr= ...; /* set local IP address + port */ bind(fd, &my_addr, sizeof(my_addr)) struct sockaddr_in to_addr = ...; connect(fd, &to_addr); /* set remote IP address + port */ /* doesn't actually communicate with remote address yet */ ... int count = write(fd, data, data_size); // OR int count = send(fd, data, data_size, 0 /* flags */); /* single message -- sent ALL AT ONCE */ int count = read(fd, buffer, buffer_size); // OR int count = recv(fd, buffer, buffer_size, 0 /* flags */); /* receives whole single message ALL AT ONCE */

## Slide 121: UDP sockets on IPv4
int fd = socket(AF_INET, SOCK_DGRAM, 0); struct sockaddr_in my_addr= ...; /* set local IP address + port */ if (0 != bind(fd, &my_addr, sizeof(my_addr))) handle_error(); ... struct sockaddr_in to_addr = ...; /* send a message to specific address */ int bytes_sent = sendto(fd, data, data_size, 0 /* flags */, &to_addr, sizeof(to_addr)); struct sockaddr_in from_addr = ...; /* receive a message + learn where it came from */ int bytes_recvd = recvfrom(fd, &buffer[0], buffer_size, 0, &from_addr, sizeof(from_addr)); ...

## Slide 122: ARP / IPv6 ND routing

## Slide 123: what about non-local machines?
when configuring network specify:
range of addresses to expect on local network
  128.148.67.0-128.148.67.255 on my desktop
  ‘‘netmask’’
gateway machine to send to for things outside my local network
  128.143.67.1 on my desktop
  my desktop looks up the corresponding MAC address

## Slide 124: routes on my desktop
$ /sbin/route -n Kernel IP routing table Destination Gateway Genmask Flags Metric Ref Use Iface 0.0.0.0 128.143.67.1 0.0.0.0 UG 100 0 0 enp0s31f6 128.143.67.0 0.0.0.0 255.255.255.0 U 100 0 0 enp0s31f6 169.254.0.0 0.0.0.0 255.255.0.0 U 1000 0 0 enp0s31f6
network configuration says:
(line 2) to get to 128.143.67.0–128.143.67.255, send directly on local network
  ‘‘genmask’’ is mask (for bitwise operations) to specify how big range is
(line 3) to get to 169.254.0.0–169.254.255.255, send directly on local network
(line 1) to get anywhere else, use ‘‘gateway’’ 128.143.67.1

## Slide 125: ARP / IPv6 ND

## Slide 126: two types of addresses?
MAC addreses: on link layer
IP addresses: on network layer
how do we know which MAC address to use?

## Slide 127: a table on my desktop
my desktop:
$ arp -an ? (128.143.67.140) at 3c:e1:a1:18:bd:5f [ether] on enp0s31f6 ? (128.143.67.236) at <incomplete> on enp0s31f6 ? (128.143.67.11) at 30:e1:71:5f:39:10 [ether] on enp0s31f6 ? (128.143.67.92) at <incomplete> on enp0s31f6 ? (128.143.67.5) at d4:be:d9:b0:99:d1 [ether] on enp0s31f6
…
network address to link-layer address + interface
only tracks things directly connected to my local network
  non-local traffic sent to local router

## Slide 128: how is that table made?
ask all machines on local network (same switch)
‘‘Who has 128.148.67.140’’
the correct one replies

## Slide 129: and HTTP? (exercise)

## Slide 130: URLs and HTTP (1)
http://www.foo.com:80/foo/bar?quux#q1
lookup IP address of www.foo.com
connect via TCP to port 80:
exercise: why include the Host there?

## Slide 131: spoofing?

## Slide 132: spoofing
if I only allow connections from my desktop’s IP addresses, how would you attack this?
hint: how do we know what address messages come from?

## Slide 133: example: echo client/server

## Slide 134: server setup

## Slide 135: connection setup: server, manual

## Slide 136: client setup

## Slide 137: connection setup: client — manual addresses

## Slide 138: read/write code

## Slide 139: echo client/server

## Slide 140: more normal connection setup

## Slide 141: connection setup: server, address setup

## Slide 142: connection setup: server, addrinfo

## Slide 143: connection setup: client, using addrinfo

## Slide 144: connection setup: lookup address

## Slide 145: other connection setup options

## Slide 146: connection setup: multiple server addresses

## Slide 147: connection setup: old lookup function
/* example hostname, portnum= "www.cs.virginia.edu", 443*/ const char *hostname; int portnum; ... struct hostent *server_ip; server_ip = gethostbyname(hostname); if (server_ip == NULL) { /* handle error */ } struct sockaddr_in addr; addr.s_addr = *(struct in_addr*) server_ip->h_addr_list[0]; addr.sin_port = htons(portnum); sock_fd = socket(AF_INET, SOCK_STREAM, IPPROTO_TCP); connect(sock_fd, &addr, sizeof(addr)); ...

## Slide 148: aside: on server port numbers
Unix convention: must be root to use ports 0–1023
  root = superuser = ‘adminstrator user’ = what sudo does
so, for testing: probably ports 1023